## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: 
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
Correlation Coefficient | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726
Chart: Statistical Alarm Plot

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: 
Rolling Standard Deviation Plot
Chart: 
Rolling Mean Plot

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through the Box- Plots, show a clear signature difference between that of normal behaviour and that of Failure with Pump Torque, Pump Efficiency, Pump Speed showing the 3 largest variances.
Rolling Std (PF=1)
Rolling Std (PF=0)
Rolling Mean (PF=1)
Rolling Mean (PF=0)

## Slide 4: Correlation analyses across datasets yield particularly interesting insights with Pump Efficiency and Volumetric Flow Meter 1,2 negatively correlated with Pump Failure in the Rolling Mean / Raw Data, whilst Horse Power and Pump Efficiency show a subsequently strong positive correlation in the Rolling Stdev Dataset.
Chart: Correlation Strength Associated With Pump Failure (Raw Data)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
 | 0.42184 | 0.26002 | 0.23319 | 0.20795 | -0.10251 | -0.10268 | -0.11211
Chart: Correlation Strength Associated With Pump Failure (Rolling Mean)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
 | 0.21805 | -0.18416 | -0.21594 | -0.30262 | -0.69243 | -0.69503 | -0.69773
Chart: Correlation Strength Associated With Pump Failure (Rolling Stdev)
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
Correlation Coefficient | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 5: Lastly, analysis of the statistical significance of variables contributing towards Pump Failure reveal that with a R Squared of 0.778, a linear model is a good fit for the data with both Rolling Mean and Rolling Standard Deviation datasets contributing key information to understand Pump Failure mechanics.
Chart: Ranking of variable significance
rank | 1 | 2 | 3 | 4 | 5 | 6 | 7